## Slide 1
SRM INSTITUTE OF SCIENCE AND TECHNOLOGY · RAMAPURAM CAMPUS
LoRa Powered Water Management System
Real-time monitoring and control across multiple tanks for smart cities

## Slide 2
The Problem with Water Management Today
Manual monitoring cannot keep pace with growing demand, spread-out tanks, and tightening resources.
Overflow & Wastage
Unmonitored tanks overflow, wasting a precious resource while other areas face shortages.
Manual Methods Fail
Float switches and dipsticks are imprecise, labor-intensive, and error-prone at scale.
Complex Infrastructure
Ultrasonic upgrades and Wi-Fi gateways demand wiring and maintenance across large areas.
Sustainability at Risk
Population growth and climate change raise the stakes for equitable water distribution.
2

## Slide 3
Building on a Rich Body of IoT Water-Monitoring Research
A survey of 26 prior works informed the design choices behind this system.
Theme | Key Contribution
IoT + cloud analytics | Sensor + microcontroller pipelines with cloud dashboards for pollution alerts (Shanmugam et al.)
Low-cost turbidity sensing | LDR/photodiode-based nephelometric turbidity detection for budget deployments (Siahaan et al.)
ESP32-based tank control | GSM/ESP32 systems preventing leakage and wastage in supply lines (Chowdhury et al.)
Edge-enabled rural systems | Ultrasonic + Blynk platforms for rural household water tanks (Manikandan et al.)
LoRa for remote quality data | Raspberry Pi + LoRa transmitting pH/TDS/temperature to remote servers (Bin Ghazali et al.)
3

## Slide 4
System Architecture at a Glance
Sensor nodes at every tank stream data through LoRa to a single gateway — no Wi-Fi, no complex wiring.
Tank Sensors
HC-SR04 ultrasonic + TDS sensor per tank
ESP32 Node
Reads, calibrates, and packetizes data
LoRa Link
433 MHz, up to 15 km line-of-sight
Cloud Storage
ThingSpeak stores & analyzes readings
Mobile App
Blynk dashboard, alerts, remote control
Data packet format: [ Turbidity/TDS (ppm), Water Level (%) ]
4

## Slide 5
Water Level Monitoring Logic
The HC-SR04 ultrasonic sensor times an echo to compute tank depth, then triggers automated pump control.
Microcontroller triggers the ultrasonic sensor
Echo return time is converted into water depth
Depth is compared against the fill-percentage thresholds
Below 25% → pump ON · Above 25% → pump OFF
Reading is packaged and transmitted via LoRa
Data is stored in the cloud and shown in the app
Non-contact & interference-resistant
25%
low-level threshold that
automatically switches the pump ON
Two-tank field tests showed synchronized level fluctuations, confirming consistent, interconnected usage patterns.
5

## Slide 6
Water Quality Monitoring with TDS Sensing
The TDS sensor detects electrical conductivity and converts it into a dissolved-solids concentration (ppm).
TDS Level | Water Quality | Remarks
0 - 150 ppm | Excellent to Good | Ideal for drinking
150 - 500 ppm | Fair to Poor | May affect taste; indicates pollution
500 - 1,000 ppm | Very Poor | Not recommended for drinking
1,000+ ppm | Unsafe | Highly contaminated
Sensor-to-Cloud Flow
›
TDS sensor reads conductivity
›
ESP32 converts to ppm value
›
Quality bracket is classified
›
Packaged with water level %
›
Transmitted via LoRa to cloud
6

## Slide 7
Why LoRa? Long Range, Low Power, No Gateway
433
MHz operating frequency
15 km
line-of-sight transmission range
1-by-1
toggle mechanism avoids collisions
LoRa vs. Alternatives
Protocol | Range | Power | Verdict
Wi-Fi | Short, needs gateways | Higher | Complex, costly at scale
Bluetooth | Very short | Low | Unsuitable for remote tanks
LoRa (433 MHz) | Up to 15 km | Very low | Chosen for this system
7

## Slide 8
From Sensor Packet to Mobile Dashboard
ThingSpeak Cloud
Central receiver forwards all tank packets directly to the cloud — no extra gateway. Data is stored with encryption and redundancy, then visualized with gauges, alerts, and trend graphs.
Blynk Mobile App
Customizable dashboards show live TDS ppm, water level %, and pump status. Users set threshold notifications and adjust settings remotely from anywhere.
Real-time gauges · Trend graphs · Threshold alerts · Remote pump control
8

## Slide 9
Results: Reliable, Synchronized, Actionable Data
Chart: Tank 1 Water Level (illustrative)
Chart: Tank 1 TDS Quality (illustrative)
Synchronized level fluctuations across two tanks confirmed interconnected, consistent usage patterns
Reliable packet delivery over LoRa with swift processing of readings
TDS thresholds flagged in real time, highlighting potential contamination early
9
Water Quality in TANK 1
Water Quality in TANK 2

## Slide 10
A Smarter, More Sustainable Path Forward
Combining ESP32 sensing with LoRa communication delivers a cost-effective, scalable system that prevents overflow, safeguards water quality, and puts control in every user's hands.
Sustainability
Reduces wastage and supports responsible resource management
Automation
Relay-driven pump control minimizes manual checks
Scalability
Multi-tank architecture with no added gateway cost
Thank You
Dept. of ECE, SRM IST
Ramapuram Campus, Chennai
10